## Slide 1: Detecting and Mitigating DoS Attack in a Network
Cisco Systems

## Slide 2: Agenda
DDoS Reality Check
Detecting
Tracing
Mitigation
Protecting the Infrastructure

## Slide 3: DDoS Vulnerabilities Multiple Threats & Targets
Peering
Point
POP
ISP Backbone
Attacked server
Z
Z
Z
Z
Z
Z
Z
Z
Z
Attack ombies:
Use valid protocols
Spoof source IP
Massively distributed
Variety of attacks
Z
Entire data center:
Servers, security devices, routers
E-commerce, web, DNS, email,…
Provider infrastructure:
DNS, routers and links
Access line
Notes: First step upstream from the local data center
Protects the link as well
Means incremental deployment only as customers sign up for service

## Slide 4: Evolution
Manually
(hack to servers)
Non critical Protocols
(eg ICMP)
Distribution Management
# Attackers
(Bandwidth)
Type of attack
Protection
Spoofed SYN
Enterprise level
Firewall/
ACL access routers
X0-X00 attackers
(X0 Mbps)
Email attach
Download from questionable site
via “chat”
ICQ, AIM, IRC
Worms
~X00-X,000
Attackers
(X00 Mbps)
Via botnets
ISP/IDC
Blackhole
ACL
DDoS solutions
All type of applicatios (HTTP, DNS, SMTP)
Spoofed SYN
Manually
Manually
Email attach
via “chat” ICQ, AIM, IRC…
~X00,000 attackers
(X-X0 Gbps)
Legitimate requests
Infrastructure elements (DNS, SMTP, HTTP…)
Blackhole (?)
ACL (?)
DDoS solutions
Anycast (?)

## Slide 5: Security Challenges The Cost of Threats
Dollar Amount of Loss By Type of Attack - CSI/FBI 2004 Survey
Notes: Prevention has real costs savings

## Slide 6: ISP Security Incident Response
ISP’s Operations Team response to a security incident can typically be broken down into six phases:
  Preparation
  Identification
  Classification
  Traceback
  Reaction
  Post Mortem
Notes: <number>

## Slide 7: Sink Hole Routers (for ISP mainly)
Use unallocated addresses
  A lot of them on the Internet… 10.0.0.0/8, 96.0.0.0/4, …
Sink hole Router locally advertises these addresses
Infected hosts will seek to contact them
Log will provide list of locally infected hosts
Will be useful for other tricks
Notes: <number>

## Slide 8: Sink Hole (aka Network Honey Pot) Set-Up
Sink Hole Router
Let’s advertise non used IP networks (in routing protocol):
0.0.0.0/8
1.0.0.0/8
96.0.0.0/4
…
Infected System
XYZ
Notes: <number>

## Slide 9: Sink Hole In Action Worm Detection
Infected System
XYZ
Sink Hole Router
Let’s infect all other hosts
Try: 96.97.98.99
IDS Sensor
The very same set-up will be used for other games
Could be used for enterprise as well
Notes: <number>

## Slide 10: Agenda
DDoS Reality Check
Detecting
Tracing
Mitigation
Protecting the Infrastructure

## Slide 11: Identification Tools
Customer/User Phone call
CPU Load on Router
SNMP – Watching the baseline and tracking variations/surges.
Netflow/IPFIX – Traffic Anomaly Detection Tools.
Sink Holes – Look for Backscatter
Notes: <number>

## Slide 12: Netflow: Statistics per TCP/UDP Flows DoS == Unusual Behavior
Real data deleted in
this presentation
Real data deleted in
this presentation
Real data deleted in
this presentation
Potential DoS attack (33 flows) on router1
Estimated: 660 pkt/s 0.2112 Mbps
ASxxx is: …
ASddd is: …
src_ip dst_ip in out src dest pkts bytes prot src_as dst_as
int int port port
192.xx.xxx.69 194.yyy.yyy.2 29 49 1308 77 1 40 6 xxx ddd
192.xx.xxx.222 194.yyy.yyy.2 29 49 1774 1243 1 40 6 xxx ddd
192.xx.xxx.108 194.yyy.yyy.2 29 49 1869 1076 1 40 6 xxx ddd
192.xx.xxx.159 194.yyy.yyy.2 29 49 1050 903 1 40 6 xxx ddd
192.xx.xxx.54 194.yyy.yyy.2 29 49 2018 730 1 40 6 xxx ddd
192.xx.xxx.136 194.yyy.yyy.2 29 49 1821 559 1 40 6 xxx ddd
192.xx.xxx.216 194.yyy.yyy.2 29 49 1516 383 1 40 6 xxx ddd
192.xx.xxx.111 194.yyy.yyy.2 29 49 1894 45 1 40 6 xxx ddd
192.xx.xxx.29 194.yyy.yyy.2 29 49 1600 1209 1 40 6 xxx ddd
192.xx.xxx.24 194.yyy.yyy.2 29 49 1120 1034 1 40 6 xxx ddd
192.xx.xxx.39 194.yyy.yyy.2 29 49 1459 868 1 40 6 xxx ddd
192.xx.xxx.249 194.yyy.yyy.2 29 49 1967 692 1 40 6 xxx ddd
192.xx.xxx.57 194.yyy.yyy.2 29 49 1044 521 1 40 6 xxx ddd
… … … … … … … … … … …

## Slide 13: Sink Hole Router Backscatter Analysis
Under DDoS victim replies to random destinations
-> Some backscatter goes to sink hole router, where it can be analysed
Notes: <number>

## Slide 14: Backscatter Analysis
Target
Ingress Routers
Other
ISPs
random sources
random sources
Sink Hole Router
random destinations
Notes: <number>

## Slide 15: Agenda
DDoS Reality Check
Detecting
Tracing
Mitigation
Protecting the Infrastructure

## Slide 16: Tracing DoS Attacks
If source prefix is not spoofed:
  -> Routing table -> Internet Routing Registry (IRR) -> direct site contact
If source prefix is spoofed:
  -> Trace packet flow through the network ACL, NetFlow, IP source tracker
  -> Find upstream ISP -> Upstream needs to continue tracing
Nowadays, 1000’s of sources not spoofed
  -> not always meaningful to trace back…
Notes: <number>

## Slide 17: Trace-Back in One Step: ICMP Backscatter
Border routers:
  Allow ICMP (rate limited)
  On packet drop, ICMP unreachable will be sent to the source
Use ACL or routing tricks (routing to NULL interface)
  All ingress router drop traffic to <victim>
  And send ICMP unreachables to spoofed source!!
Sink hole router logs the ICMPs!
Notes: <number>

## Slide 18: Trace-Back Made Easy: ICMP Backscatter Step 1: no drop
Target
Ingress Routers
Other
ISPs
random sources
random sources
Sink hole Router

## Slide 19: Trace-Back Made Easy: ICMP Backscatter Step 2: Drop Packets
Target
Ingress Routers
Other
ISPs
Sink hole Router
with logging
ICMP unreachables

## Slide 20: Agenda
DDoS Reality Check
Detecting
Tracing
Mitigation
Protecting the Infrastructure

## Slide 21: At the Edge / Firewalls ACL/QoS to Drop/Throttle DDoS Traffic
Server1
Target
Server2
.
.
.
.
.
.
.
.
R3
R1
R2
R5
R4
R
R
R
1000
1000
FE
peering
100
Easy to choke
Point of failure
Not scalable
Consumer tuned
Too late

## Slide 22: At the Routers in the Network ACL/QoS to Drop/Throttle DDoS Traffic
Server1
Victim
Server2
.
.
.
.
.
.
.
.
R3
R1
R2
R5
R4
R
R
R
1000
1000
FE
peering
100
Rand. Spoofing?
Throws good with bad
~X0,000 ACLs?
ACLs,
Upper bound on traffic

## Slide 23: Black Holing the DoS Traffic Re-Directing Traffic to the Victim
Target
Ingress Routers
Other
ISPs
Sink hole Router: Announces route “target/32”
Logging!!
Keeps line to customer clear
But cuts target host off completely
Discuss with customer!!!
Just for analysis normally

## Slide 24: Identifying and Dropping only DDoS Traffic/1
Protected Zone 1: Web
Protected Zone 2: Name Servers
Protected Zone 3: E-Commerce Application
Cisco Traffic Anomaly Detector Module (or Cisco IDS or third- party system)
Cisco Anomaly Guard Module

## Slide 25: Identifying and Dropping only DDoS Traffic/2
Protected Zone 1: Web
Protected Zone 2: Name Servers
Protected Zone 3: E-Commerce Application
Cisco Traffic Anomaly Detector Module
Cisco Anomaly Guard Module
1. Detect
Target

## Slide 26: Identifying and Dropping only DDoS Traffic/3
Protected Zone 1: Web
Protected Zone 2: Name Servers
Protected Zone 3: E-Commerce Application
Cisco Traffic Anomaly Detector Module
Cisco Anomaly Guard Module
1. Detect
Target
2. Activate: Auto/Manual

## Slide 27: Identifying and Dropping only DDoS Traffic/4
Protected Zone 1: Web
Protected Zone 2: Name Servers
Protected Zone 3: E-Commerce Application
Cisco Traffic Anomaly Detector Module
Cisco Anomaly Guard Module
1. Detect
Target
2. Activate: Auto/Manual
3. Divert only
target’s traffic
Route update:
RHI internal, or BGP/other external

## Slide 28: Identifying and Dropping only DDoS Traffic/5
Protected Zone 1: Web
Protected Zone 2: Name Servers
Protected Zone 3: E-Commerce Application
Cisco Traffic Anomaly Detector Module
Cisco Anomaly Guard Module
1. Detect
Target
2. Activate: Auto/Manual
3. Divert only
target’s traffic
4. Identify and filter malicious traffic
Traffic Destined
to the Target

## Slide 29: Identifying and Dropping only DDoS Traffic/6
Protected Zone 1: Web
Protected Zone 2: Name Servers
Protected Zone 3: E-Commerce Application
Cisco Traffic Anomaly Detector Module
Cisco Anomaly Guard Module
1. Detect
Target
2. Activate: Auto/Manual
3. Divert only
target’s traffic
4. Identify and filter malicious traffic
Traffic Destined
to the Target
Legitimate Traffic to Target
5. Forward legitimate traffic

## Slide 30: Identifying and Dropping only DDoS Traffic/7
Protected Zone 1: Web
Protected Zone 2: Name Servers
Protected Zone 3: E-Commerce Application
Cisco Traffic Anomaly Detector Module
Cisco Anomaly Guard Module
1. Detect
Target
2. Activate: Auto/Manual
3. Divert only
target’s traffic
4. Identify and filter malicious traffic
Traffic Destined
to the Target
Legitimate Traffic to Target
5. Forward legitimate traffic
6. Non-targeted traffic flows freely

## Slide 31
  Active Verification
  Statistical
  Analysis
Layer 7
Analysis
  Rate Limiting
Multi-Verification Process (MVP)
Integrated Defenses in the Guard XT
Legitimate + attack traffic to target
Dynamic &
Static Filters
Detect anomalous behavior & identify precise attack flows and sources
Notes: To stop all types of attacks key is multiple layers of defense
All within the Guard
Core is anomaly recognition – behavior not string signature based; off of normal profile not specific known attacks
This core of anomaly recognition is basically the subset in the Detector without the enforcement layers.

## Slide 32
  Active Verification
  Statistical
  Analysis
Layer 7
Analysis
  Rate Limiting
Legitimate + attack traffic to target
Dynamic &
Static Filters
Apply anti-spoofing
to block malicious flows
Multi-Verification Process (MVP)
Integrated Defenses in the Guard XT
Notes: Intelligently and selectively applied anti-spoofing, at multiple levels, until all spoofed packets are determined to be dropped
If continue to see anomaly, then can be sure of malicious source

## Slide 33: Anti-Spoofing Example – http/TCP
SrcIP, Source IP
Guard
Syn(c#)
Synack(c#’,s#’)
Hash-function(SrcIP,port,t)
ack(c#,s#)
SrcIP,port#
=
Redirect(c#,s#)
Syn(c#’)
request(c#’,s#’)
Victim
Verified connections
synack(c#,s#)

## Slide 34
  Active Verification
  Statistical
  Analysis
Layer 7
Analysis
  Rate Limiting
Dynamic &
Static Filters
Legitimate traffic
Multi-Verification Process (MVP)
Integrated Defenses in the Guard XT
Dynamically insert specific filters to block attack flows & sources
Apply rate limits

## Slide 35: Measured Response
Detection
Passive copy of traffic monitoring
Analysis
Diversion for more granular in-line analysis
Flex filters, static filters and bypass in operation
All flows forwarded but analyzed for anomalies
Basic Protection
Basic anti-spoofing applied
Analysis for continuing anomalies
Strong Protection
Strong anti-spoofing (proxy) if appropriate
Dynamic filters deployed for zombie sources
Anomaly
Verified
Learning
Periodic observation of patterns to update baseline profiles
Attack
Detected
Anomaly
Identified
Notes: In addition to the multiple planes of defense, there are also escalating levels of defense
Escalation minimizes false positives, makes defenses as transparent as possible, and conserves resources for maximizing performance
The filters in the Analysis stage are basically pre-emptive “lockdown” type filters statically pre-determined as opposed to dynamically driven by actual recognition of anomalies.
The embedded analysis in the Guard enables it to be confidently used with other detection systems besides the Detector.

## Slide 36: Agenda
DDoS Reality Check
Detecting
Tracing
Mitigation
Protecting the Infrastructure

## Slide 37: Three Planes, Definition
A device typically consists of
  Data/forwarding Plane: the useful traffic
  Control Plane: routing protocols, ARP, …
  Management Plane: SSH, SNMP, …
In these slides Control Plane refers to all the Control/Management plane traffic destined to the device.
Hardware
Software

## Slide 38: Control Plane Overrun
Loss of protocol keep-alives:
  line go down
  route flaps
  major network transitions.
Loss of routing protocol updates:
  route flaps
  major network transitions.
Near 100% CPU utilization
  Can prevent other high priority tasks

## Slide 39: Need for Control Plane Policing
Classify all Control Plane traffic in multiple classes
Each class is capped to a certain amount
Fair share for each classes or each source in each classes
   one class cannot overflow the others
   even an ICMP flood to the router won’t affect routing

## Slide 40
Q and A
<number>
<number>
<number>
Notes: <number>

## Slide 41
<number>
<number>
<number>