## Slide 1: IP Telephony Security
Cisco Systems

## Slide 2: Threat Models Merge
IP Telephony inherits IP data network threat models:
  Reconnaissance, DoS, host vulnerability exploit, surveillance, hijacking, identity, theft, misuse, etc.
QoS requirements of IP Telephony increase exposure to DoS attacks that affect:
  Delay, jitter, packet loss, bandwidth
PC endpoints typically require user authentication, phones typically allow any user (exceptions: access/billing codes, Class of Service)

## Slide 3: Making IP Telephony Secure
Put a protective shell around IP through the infrastructure
  Protecting routers & switches
  Preventing layer 2 tricks like VOMIT
  Physical security!
  Protecting IPT servers
Put security in the IP telephony protocols
The above are not mutually exclusive!

## Slide 4: Protect Routers and Switches
Apply well-known and proven techniques to protect network elements
  Follow sound password and authentication practices
  Ensure that unused router services are turned off
  Securely configure any network management functions
  NTP Authentication, Routing Authentication, Password encryption, SSH, AAA features, access control for SNMP, block telnet, turn off unused TCP/UDP service
  Restrict Physical Access! Beware router/switch password recovery.
  …

## Slide 5: Prevent Layer 2 Tricks
CAM is the forwarding table for a switch
  Filled dynamically based on source MAC address
  If destination MAC address is unknown => flood frame within VLAN
  CAM overflow: sends zillions of fake source MAC to fill MAC => learning is disabled
  Prevention: port security (small and finite number of MAC per port)
DHCP
  Rogue DHCP: malicious (fake DNS, GW) allows for Man in the Middle Attacks
  Prevention: DHCP snooping, drop all replies coming from non trusted DHCP servers
ARP is the protocol to link MAC & IP addresses
  ARP spoofing: attacked sends fake binding his-MAC, sniffed-IP
  Prevention: DHCP snooping to learn trusted binding, drop all violation
Spanning Tree Protocol, the ‘routing’ protocol, detects loops
  Fake BPDU => re-routing, computation (DoS)
  Prevention: drop BPDU on all access port, partially static topology

## Slide 6: A Word About Physical Security
Access to network equipment must be controlled
Keep network equipment well within recommended environmental limits
Mission critical resources may require dispersion, to provide effective redundancy
Killing power is an effective DoS attack

## Slide 7: IPT Servers
They are essential to IPT
Protected by
  Strict security policy enforcement (firewall, …)
  Host security: IPS, AV, …
  Applying security fixes
  RBAC management

## Slide 8: Securing IPT Protocols First Step: Phone Authentication
Using X.509 certificates
Manufacturing Installed Certificate (MIC)
  Installed in non-erasable, non-volatile memory
Locally Significant Certificate (LSC)
  Installed by local authority
  Supercedes MIC

## Slide 9: Securing IPT Protocols Second Step: Use TLS for Signaling
IP
TCP
TLS
HTTP
SCCP
FTP
SIP
Supports any application protocol
Bi-directional PKI establishes Identity
HMAC provides Integrity
Encryption offers Privacy

## Slide 10: Securing IPT Protocols Second Step: Use TLS for Signaling
TLS is the transport for signed (RSA), authenticated (HMAC-SHA1) and encrypted (AES-128) signaling (1)

## Slide 11: Securing IPT Protocols Third Step: Use SRTP for Audio Stream
Authenticated portion
timestamp
P
V
X
CC
M
PT
sequence number
synchronization source (SSRC) identifier
contributing sources (CCRC) identifiers …
RTP extension (optional)
RTP payload
SRTP MKI -- 0 bytes for voice
Authentication tag -- 4 bytes for voice
Encrypted portion
Secure Real Time Protocol
RFC 3711 for transport of secure media
Uses AES-128 for both authentication and encryption

## Slide 12: Securing IPT Protocols Third Step: Use SRTP for Audio Stream
SRTP is the transport for authenticated and encrypted (AES-128) media (2)

## Slide 13: Conclusion
Security for IPT is usually desirable
Security for IPT can be delivered
  Within the network infrastructure
  By the IPT protocols
Security is not a barrier for deployment
BTW: apply the same paranoia to data as well